## Slide 1: Lecture 01 Number Systems
CSE115: Computing Concepts

## Slide 2: Introduction to Numbering Systems
Base: The number of fundamental symbols in a numbering system (e.g. 0, 1, 2 etc.)
We are all familiar with the decimal number system (Base 10). Some other number systems that we will work with are:
  Binary  Base 2
  Octal  Base 8
  Hexadecimal  Base 16

## Slide 3: Common Number Systems
System | Base | Symbols | Used by humans? | Used in computers?
Decimal | 10 | 0, 1, … 9 | Yes | No
Binary | 2 | 0, 1 | No | Yes
Octal | 8 | 0, 1, … 7 | No | No
Hexa- decimal | 16 | 0, 1, … 9, A, B, … F | No | No
Decimal numbers are used by humans
Binary numbers are used by computers
Octal and Hexa-decimal numbers are useful to represent long
binary numbers in short form

## Slide 4: Lets do some counting (1 of 3)
Decimal | Binary | Octal | Hexa- decimal
0 | 0 | 0 | 0
1 | 1 | 1 | 1
2 | 10 | 2 | 2
3 | 11 | 3 | 3
4 | 100 | 4 | 4
5 | 101 | 5 | 5
6 | 110 | 6 | 6
7 | 111 | 7 | 7

## Slide 5: Lets do some counting (2 of 3)
Decimal | Binary | Octal | Hexa- decimal
8 | 1000 | 10 | 8
9 | 1001 | 11 | 9
10 | 1010 | 12 | A
11 | 1011 | 13 | B
12 | 1100 | 14 | C
13 | 1101 | 15 | D
14 | 1110 | 16 | E
15 | 1111 | 17 | F

## Slide 6: Lets do some counting (3 of 3)
Decimal | Binary | Octal | Hexa- decimal
16 | 10000 | 20 | 10
17 | 10001 | 21 | 11
18 | 10010 | 22 | 12
19 | 10011 | 23 | 13
20 | 10100 | 24 | 14
21 | 10101 | 25 | 15
22 | 10110 | 26 | 16
23 | 10111 | 27 | 17
Etc.

## Slide 7: Bits and Bytes
A single binary digit is called a bit.
A collection of 8 bits is called a byte.
There are 2 fundamental digits in the binary number system. One of them is 0 and the other is 1.

## Slide 8: Write the base as subscript
2510 = 110012 = 318 = 1916
Base

## Slide 9: Conversion Among Bases
The possibilities:
Hexadecimal
Decimal
Octal
Binary

## Slide 10
12510 => 5 x 100 = 5 2 x 101 = 20 1 x 102 = 100 125
Base
Weight
A closer look at a decimal number

## Slide 11: Binary to Decimal
Hexadecimal
Decimal
Octal
Binary

## Slide 12: Binary to Decimal
Technique
  Multiply each bit by 2n, where n is the “weight” of the bit
  The weight is the position of the bit, starting from 0 on the right
  Add the results

## Slide 13: Example
1010112 => 1 x 20 = 1 1 x 21 = 2 0 x 22 = 0 1 x 23 = 8 0 x 24 = 0 1 x 25 = 32
4310
Bit “0”

## Slide 14: Octal to Decimal
Hexadecimal
Decimal
Octal
Binary

## Slide 15: Octal to Decimal
Technique
  Multiply each bit by 8n, where n is the “weight” of the bit
  The weight is the position of the bit, starting from 0 on the right
  Add the results

## Slide 16: Example
7248 => 4 x 80 = 4 2 x 81 = 16 7 x 82 = 448 46810

## Slide 17: Hexadecimal to Decimal
Hexadecimal
Decimal
Octal
Binary

## Slide 18: Hexadecimal to Decimal
Technique
  Multiply each bit by 16n, where n is the “weight” of the bit
  The weight is the position of the bit, starting from 0 on the right
  Add the results

## Slide 19: Example
ABC16 => C x 160 = 12 x 1 = 12 B x 161 = 11 x 16 = 176 A x 162 = 10 x 256 = 2560
274810

## Slide 20: Decimal to Binary
Hexadecimal
Decimal
Octal
Binary

## Slide 21: Decimal to Binary
Technique
  Divide by two, keep track of the remainder
  First remainder is bit 0 (LSB, least-significant bit)
  Second remainder is bit 1
  Etc.

## Slide 22: Example
12510 = ?2
2 125 62 1
2 31 0
2 15 1
2 7 1
2 3 1
2 1 1
2 0 1
12510 = 11111012

## Slide 23: Decimal to Octal
Hexadecimal
Decimal
Octal
Binary

## Slide 24: Decimal to Octal
Technique
  Divide by 8
  Keep track of the remainder

## Slide 25: Example
123410 = ?8
8 1234
154 2
8
19 2
8
2 3
8
0 2
123410 = 23228

## Slide 26: Decimal to Hexadecimal
Hexadecimal
Decimal
Octal
Binary

## Slide 27: Decimal to Hexadecimal
Technique
  Divide by 16
  Keep track of the remainder

## Slide 28: Example
123410 = ?16
123410 = 4D216
16 1234
77 2
16
4 13 = D
16
0 4

## Slide 29: Octal to Binary
Hexadecimal
Decimal
Octal
Binary

## Slide 30: Octal to Binary
Technique
  Convert each octal digit to a 3-bit equivalent binary representation

## Slide 31: Example
7058 = ?2
7 0 5
111 000 101
7058 = 1110001012

## Slide 32: Binary to Octal
Hexadecimal
Decimal
Octal
Binary

## Slide 33: Binary to Octal
Technique
  Group bits in threes, starting on right
  Convert to octal digits

## Slide 34: Example
10110101112 = ?8
1 011 010 111
1 3 2 7
10110101112 = 13278

## Slide 35: Hexadecimal to Binary
Hexadecimal
Decimal
Octal
Binary

## Slide 36: Hexadecimal to Binary
Technique
  Convert each hexadecimal digit to a 4-bit equivalent binary representation

## Slide 37: Example
10AF16 = ?2
1 0 A F
0001 0000 1010 1111
10AF16 = 00010000101011112

## Slide 38: Binary to Hexadecimal
Hexadecimal
Decimal
Octal
Binary

## Slide 39: Binary to Hexadecimal
Technique
  Group bits in fours, starting on right
  Convert to hexadecimal digits

## Slide 40: Example
10101110112 = ?16
10 1011 1011
B B
10101110112 = 2BB16

## Slide 41: Octal to Hexadecimal
Hexadecimal
Decimal
Octal
Binary

## Slide 42: Octal to Hexadecimal
Technique
  Use binary as an intermediary

## Slide 43: Example
10768 = ?16
1 0 7 6
001 000 111 110
2 3 E
10768 = 23E16

## Slide 44: Hexadecimal to Octal
Hexadecimal
Decimal
Octal
Binary

## Slide 45: Hexadecimal to Octal
Technique
  Use binary as an intermediary

## Slide 46: Example
1F0C16 = ?8
1 F 0 C
0001 1111 0000 1100
1 7 4 1 4
1F0C16 = 174148

## Slide 47: Conversion Exercise
Try not to use a calculator!
Decimal | Binary | Octal | Hexa- decimal
33 |  |  | 
 | 1110101 |  | 
 |  | 703 | 
 |  |  | 1AF

## Slide 48: Conversion Exercise
Decimal | Binary | Octal | Hexa- decimal
33 | 100001 | 41 | 21
117 | 1110101 | 165 | 75
451 | 111000011 | 703 | 1C3
431 | 110101111 | 657 | 1AF
Answer

## Slide 49: Common Powers (1 of 2)
Base 10
Power | Preface | Symbol
10-12 | pico | p
10-9 | nano | n
10-6 | micro | 
10-3 | milli | m
103 | kilo | k
106 | mega | M
109 | giga | G
1012 | tera | T
Value
.000000000001
.000000001
.000001
.001
1000
1000000
1000000000
1000000000000

## Slide 50: Common Powers (2 of 2)
Base 2
Power | Preface | Symbol
210 | kilo | k
220 | mega | M
230 | Giga | G
Value
1024
1048576
1073741824
What is the value of “k”, “M”, and “G”?
In computing, particularly w.r.t. memory, the base-2 interpretation generally applies

## Slide 51: Example
/ 230 =
In the lab… 1. Double click on My Computer 2. Right click on C: 3. Click on Properties

## Slide 52: Complement
Complement is the negative equivalent of a number.
If we have a number N then complement of N will give us another number which is equivalent to –N
So if complement of N is M, then we can say M = -N
So complement of M = -M = -(-N) = N
So complement of complement gives the original number

## Slide 53: Types of Complement
For a number of base r, two types of complements can be found
  1. r’s complement
  2. (r-1)’s complement
Definition:
  If N is a number of base r having n digits then
    r’s complement of N = rn – N and
    (r-1)’s complement of N = rn-N-1

## Slide 54: Example
Suppose N = (3675)10
So we can find two complements of this number. The 10’s complement and the 9’s complement. Here n = 4
10’s complement of (3675) = 104 - 3675
= 6325
9’s complement of (3675) = 104 - 3675 -1
= 6324

## Slide 55: Short cut way to find (r-1)’s complement
In the previous example we see that 9’s complement of 3675 is 6324. We can get the result by subtracting each digit from 9.
Similarly for other base, the (r-1)’s complement can be found by subtracting each digit from r-1 (the highest digit in that system).
For binary 1’s complement is even more easy. Just change 1 to 0 and 0 to 1. (Because 1-1=0 and 1-0=1)

## Slide 56: Example
Find the (r-1)’s complement in short cut method.
  (620143)8 Ans: 157634
  (A4D7E)16 Ans: 5B281
  (110100101)2 Ans: 001011010

## Slide 57: Short cut way to find r’s complement
From the definition we can say,
  r’s complement of (N) = (r-1)’s complement +1
So, we can first find the (r-1)’s complement in short cut way then add 1 to get the r’s complement.
Example: r’s complement of (620143)8 =157634 + 1
= 157635
This method is a two step process. But we can find it in a one step process also.

## Slide 58: Short cut way to find r’s complement
One step process:
  Start from rightmost digit to left.
  Initial zeros will remain unchanged
  Rightmost non-zero digit will be subtracted from r
  Rest of the digits will be subtracted from r-1
Example:
  Find the 10’s complement of (529400)10
  Rightmost 2 zeros will not change, 4 will be subtracted from 10 and rest of the digits 529 will be subtracted from 9
  So the result is 470600

## Slide 59: Example
Find the r’s complement in short cut method.
  (8210)10 Ans: 1790
  (61352)10 Ans: 38648
  (6201430)8 Ans: 1576350
  (A4D7E0)16 Ans: 5B2820

## Slide 60: Example for binary
For binary: start from rightmost bit
Up to first 1 – no change.
For rest of the bits toggle (Change 1 to 0 and 0 to 1)
  (11010010100)2 Ans: 00101101100
  (01101001011)2 Ans: 10010110101
  (10000000)2 Ans: 10000000